## Slide 1
SG GoAssist
Autonomous Passenger Assistance System
National University of Singapore (NUS)
Team: SmaRHt Buses
Jin Donghua, Liu Xuan Tong, Ryan Koh Jun Hao,
Sim Hong Meng, Zeph Tang Zhenkai
Staff-in-charge: Koenraad Mouthaan
Draft progress as of 25 September 2026
Notes: Official guideline: ../SGBTGC 2026 - IHL Updates 18 Aug 2026.pdf, pp. 16–18 (18 August 2026 update).
5-minute core presentation. Planned speaking time: 15 seconds.
Presenter cue: Introduce SG GoAssist from NUS team SmaRHt Buses. Members: Jin Donghua, Liu Xuan Tong, Ryan Koh Jun Hao, Sim Hong Meng and Zeph Tang Zhenkai. Staff-in-charge: Koenraad Mouthaan.
Primary source: ../SG_GoAssist_Prototype_Action_Plan.pdf, p. 1. Institution and team metadata confirmed by the user.
Core slides 1–8 total 300 seconds. All following slides are Q&A appendices, outside the timed presentation. A separate video of up to 5 minutes is allowed and remains to be produced. Presenter: ____________________

## Slide 2
Problem and project objective
A controlled prototype for accessible boarding and alighting
02
Passenger need
A clear way to request help and understand when boarding or alighting can proceed.
Project objective
Complete one repeatable journey from explicit request to acknowledgement, safe assistance and verified completion.
Inclusive scope
Ramp assistance, extra time and audio, visual or haptic guidance based on the passenger’s choice.
Notes: Official guideline: ../SGBTGC 2026 - IHL Updates 18 Aug 2026.pdf, pp. 16–18 (18 August 2026 update).
5-minute core presentation. Planned speaking time: 30 seconds.
Presenter cue: Explain that requests must lead to understandable, verified assistance. Include passengers who ask for extra time or guidance without a visible mobility aid. State the controlled-prototype boundary.
Primary source: ../SG_GoAssist_Prototype_Action_Plan.pdf, pp. 1–3, 13.
Presenter: ____________________
Status date: 25 September 2026. Blank result fields are intentionally incomplete.

## Slide 3
Alternatives and selected method
03
Approach | Useful feature | Tradeoff / design decision
Manual assistance | Human judgement and flexible intervention | Use as the baseline. It requires an operator to coordinate each journey.
Camera-only trigger | Observable assistance cues without app input | A cue cannot establish a request or consent. Reject as ramp authority.
Explicit request with sensor checks | Passenger control plus verified system response | Selected method. Adds integration and calibration work.
ML interprets uncertain scenes. Fixed rules and physical sensors retain safety vetoes.
Notes: Official guideline: ../SGBTGC 2026 - IHL Updates 18 Aug 2026.pdf, pp. 16–18 (18 August 2026 update).
5-minute core presentation. Planned speaking time: 40 seconds.
Presenter cue: Compare design tradeoffs, not measured impact. Manual assistance provides an operator baseline. Camera-only triggering cannot establish consent. Explain why explicit intent with perception and deterministic checks is the selected prototype method.
Primary source: ../SG_GoAssist_Prototype_Action_Plan.pdf, pp. 2, 5–9, 13. Comparison is the team design rationale, not a completed experimental comparison.
Presenter: ____________________
Status date: 25 September 2026. Blank result fields are intentionally incomplete.

## Slide 4
Integrated system and safety principle
04
Layer | Role in the assistance journey
App and stop unit | Record request, confirmation and cancellation for the selected bus.
Camera and VL53L0X | Report camera cues, single-zone range and sensor health.
Backend and operator | Manage the case, expose reasons and apply safety rules.
Mock-bus controller | Repeat local interlocks and verify ramp limit-switch state.
Confirmed intent + fresh safety inputs + verified position
Uncertainty blocks movement. Completion requires a verified stowed ramp.
Notes: Official guideline: ../SGBTGC 2026 - IHL Updates 18 Aug 2026.pdf, pp. 16–18 (18 August 2026 update).
5-minute core presentation. Planned speaking time: 40 seconds.
Presenter cue: Walk through the four layers. Emphasize that perception supports a confirmed request. The controller repeats safety checks during movement and verifies deployed and stowed positions.
Primary source: ../SG_GoAssist_Prototype_Action_Plan.pdf, pp. 3, 9; docs/grand-challenge-integrated-prototype.md, Safety policy; docs/task-requirements-traceability.md. Software logic exists, but physical integration acceptance remains incomplete. VL53L0X threshold calibration, range/status contract adaptation and controller fault tests remain pending. Sensor specification: STMicroelectronics VL53L0X product page https://www.st.com/en/imaging-and-photonics-solutions/vl53l0x.html and DS11555 Rev 6 https://www.st.com/resource/en/datasheet/vl53l0x.pdf (pp. 1, 21–24). Single-zone ranging gives one distance per reading over I2C. The 940 nm emitter is infrared. Up to 2 m is a conditional manufacturer specification, not verified prototype range. One reading cannot prove the full ramp area clear. Visible RYS1230 marking lasers are separate from the ToF sensor.
Presenter: ____________________
Status date: 25 September 2026. Blank result fields are intentionally incomplete.

## Slide 5
Original project contributions
Originality claim is limited to the team’s design and integration work
05
Intent and assistance workflow
Retain passenger choice across request, confirmation, cancellation, actuation and verified completion.
Safety and accessible feedback integration
Connect case decisions, local interlocks, position checks and passenger/operator status in one auditable loop.
Centre-door mechanism concept
Develop the door, ramp and boarding-fixture CAD arrangement and operating sequence for the prototype.
Reused foundations: ESP32, ToF sensors, pretrained detection and ArUco methods.
Notes: Official guideline: ../SGBTGC 2026 - IHL Updates 18 Aug 2026.pdf, pp. 16–18 (18 August 2026 update).
5-minute core presentation. Planned speaking time: 40 seconds.
Presenter cue: Separate reused technologies from the team work. The proposed contribution is the combined intent-to-outcome assistance workflow and its safety/feedback integration. Avoid world-first claims. Judges assess only original elements, so retain implementation and authorship evidence.
Official guideline: ../SGBTGC 2026 - IHL Updates 18 Aug 2026.pdf, pp. 16–18 (18 August 2026 update). Originality and Creativity carries 30%. Primary source: ../SG_GoAssist_Prototype_Action_Plan.pdf, pp. 2–3, 9; docs/grand-challenge-integrated-prototype.md; cad/VALIDATION_v2.md. These are scoped project contributions, not a prior-art novelty assessment.
Presenter: ____________________
Status date: 25 September 2026. Blank result fields are intentionally incomplete.

## Slide 6
Progress supported by current evidence
06
Software
App, backend and operator flow with mock test evidence.
CAD
73 sampled poses. Zero moving-part intersections in a discrete check.
Sensor bench
27 consecutive valid VL53L0X samples, 30–136 mm after power cycle.
Physical integration and measured ML performance remain incomplete.
VL53L0X covers a limited field. Accuracy and physical ramp coverage remain unverified.
Notes: Official guideline: ../SGBTGC 2026 - IHL Updates 18 Aug 2026.pdf, pp. 16–18 (18 August 2026 update).
5-minute core presentation. Planned speaking time: 60 seconds.
Presenter cue: Distinguish software, CAD and the sensor bench. Software has documented automated tests and fixture/mock operation. The CAD check is discrete packaging evidence. Explain the 27 valid sensor samples and that accuracy is unverified. Explain the selected VL53L0X single-zone field and the remaining calibration, firmware adaptation, physical and ML evidence.
Sources: docs/feature-readiness-matrix.md; docs/grand-challenge-integrated-prototype.md; cad/VALIDATION_v2.md; hardware/esp32-s3-tof-test/README.md; artifacts/apas-tof-build/serial-powercycle-test.txt; hardware/edge-observer/ml1/README.md. Image: cad/Punggol_WeRide_Robobus_v2_deployed.png, project CAD render. No full software rerun or physical integration trial performed for this draft. Sensor specification: STMicroelectronics VL53L0X product page https://www.st.com/en/imaging-and-photonics-solutions/vl53l0x.html and DS11555 Rev 6 https://www.st.com/resource/en/datasheet/vl53l0x.pdf (pp. 1, 21–24). Single-zone ranging gives one distance per reading over I2C. The 940 nm emitter is infrared. Up to 2 m is a conditional manufacturer specification, not verified prototype range. One reading cannot prove the full ramp area clear. Visible RYS1230 marking lasers are separate from the ToF sensor.
Presenter: ____________________
Status date: 25 September 2026. Blank result fields are intentionally incomplete.

## Slide 7
Validation plan and results
07
Test | Original target | Result
Request | 20/20 delivery trials, acknowledgement within 2 s | 
Assistance cue | At least 90% wheelchair/PMA recall, at least 10 FPS | 
Safety and actuation | Zero missed obstructions. 50 cycles without binding | 
Docking and journey | 10 docking trials. At least 9/10 cold-start journeys | 
Dwell | No premature CLEAR in defined tests | 
Impact and accessibility findings:
____________________________________________
Notes: Official guideline: ../SGBTGC 2026 - IHL Updates 18 Aug 2026.pdf, pp. 16–18 (18 August 2026 update).
5-minute core presentation. Planned speaking time: 40 seconds.
Presenter cue: State these are planned targets. Blank fields await measured results. Compare the same journey with manual assistance and collect consented feedback. Explain that physical trials must demonstrate both successful assistance and safe failure responses.
Primary source: ../SG_GoAssist_Prototype_Action_Plan.pdf, pp. 12–13. Original targets shown. Later docs/task-requirements-traceability.md adds 30 requests per explicit source and acknowledgement P95 under 2 seconds. Confirm the final protocol. Results intentionally blank.
Presenter: ____________________
Status date: 25 September 2026. Blank result fields are intentionally incomplete.

## Slide 8
Remaining work and competition milestones
08
Next: calibrate VL53L0X, adapt controller thresholds and fault logic, then test.
Official milestone | Date
Project report and display-poster artwork | 30 September 2026
Pre-event prototype showcase (25 minutes) | 7 October 2026
Main-event slideshow and video submission | 15 October 2026
Main event: presentation, video and Q&A | 24 October 2026
Dates are tentative. Main-event format: 5 min talk, up to 5 min video, 5 min Q&A.
Core presentation ends here. Supporting slides follow for Q&A.
Notes: Official guideline: ../SGBTGC 2026 - IHL Updates 18 Aug 2026.pdf, pp. 16–18 (18 August 2026 update).
5-minute core presentation. Planned speaking time: 35 seconds.
Presenter cue: Close with the next milestone: a repeatable physical journey supported by measured evidence. State official dates carefully. The report and poster are due in September, while slideshow/video submission is in October. The organiser labels dates tentative.
Official guideline: ../SGBTGC 2026 - IHL Updates 18 Aug 2026.pdf, pp. 16–18 (18 August 2026 update). pp. 16–17. Action-plan 27 September content freeze is an internal planning target, not an organiser deadline. Main event permits 5-minute presentation, up to 5-minute video and 5-minute Q&A. Separate video remains incomplete.
Presenter: ____________________
Status date: 25 September 2026. Blank result fields are intentionally incomplete.

## Slide 9
Appendix A. Intended journey
09
Stage | Passenger or system action | Required outcome
1 Request and recognise | Select assistance and bus. Perception adds cues. | Explicit intent remains authoritative.
2 Prepare and dock | Reserve dwell and align with the boarding fixture. | Correct bus, stop and ramp reach.
3 Mark and check | Mark area. Check camera and VL53L0X inputs. | Clear, fresh safety inputs.
4 Deploy and board | Open door, deploy ramp and maintain dwell. | Verify deployed position and monitor interlocks.
5 Complete | Retract, verify stowed and close the door. | Save outcome or escalate a fault.
Second demonstration scenario: extra time and guidance without a ramp request.
Notes: Q&A appendix. Outside the timed 5-minute core presentation.
Primary source: ../SG_GoAssist_Prototype_Action_Plan.pdf, p. 3. The original nine steps are request, recognise, prepare, dock, mark zone, check zone, deploy, board and complete. Current physical end-to-end completion has not been established. The camera interprets the scene and VL53L0X provides a single-zone range check in a limited monitored field. One range does not establish full-area clearance. Sensor specification: STMicroelectronics VL53L0X product page https://www.st.com/en/imaging-and-photonics-solutions/vl53l0x.html and DS11555 Rev 6 https://www.st.com/resource/en/datasheet/vl53l0x.pdf (pp. 1, 21–24). Single-zone ranging gives one distance per reading over I2C. The 940 nm emitter is infrared. Up to 2 m is a conditional manufacturer specification, not verified prototype range. One reading cannot prove the full ramp area clear. Visible RYS1230 marking lasers are separate from the ToF sensor.
Presenter: ____________________
Status date: 25 September 2026. Blank result fields are intentionally incomplete.

## Slide 10
Appendix B. Architecture and authority
Shared messages connect software, sensing and the mock bus
10
Layer | Main components | Responsibility
Passenger | App, tactile stop unit, optional NFC | Record request, confirmation and cancellation.
Perception | Camera, edge observer, VL53L0X | Publish camera cues, one range and sensor health.
Decision | Backend case state machine, operator console | Match the case and apply deterministic safety gates.
Vehicle | ESP32 controller, ramp/door, limit switches | Repeat local interlocks and verify motion outcome.
Only passenger or operator confirmation establishes ramp intent.
ML supports decisions. It cannot override a safety interlock.
Notes: Q&A appendix. Outside the timed 5-minute core presentation.
Primary source: ../SG_GoAssist_Prototype_Action_Plan.pdf, pp. 5, 9; docs/grand-challenge-integrated-prototype.md, Safety policy and Portable build; docs/task-requirements-traceability.md, SR-01–04.
Presenter: ____________________
Status date: 25 September 2026. Blank result fields are intentionally incomplete.

## Slide 11
Appendix C. Software evidence
The repository implements the competition software loop
11
Passenger and operator interfaces
Request assistance, track case status, cancel and expose reasons for blocked or escalated actions.
Backend and mock control
Persist cases and audit events. Reject duplicate actions and verify deployed/stowed telemetry.
Verification still required
Physical actuation and on-device ARM64 Qwen tests. Transport arrivals and selected amenities use labelled fixtures.
Notes: Q&A appendix. Outside the timed 5-minute core presentation.
Sources: README.md, Integrated assistance demonstrator and Private hybrid assistant; docs/grand-challenge-integrated-prototype.md; docs/feature-readiness-matrix.md. No assertion that all tests were rerun for this report.
Presenter: ____________________
Status date: 25 September 2026. Blank result fields are intentionally incomplete.

## Slide 12
Appendix D. VL53L0X capability and evidence
ESP32-S3 and VL53L0X live ranging verified on 23 September
12
27 consecutive valid samples
30–136 mm after a full sensor power cycle
Selected sensor capability
One distance per reading over I²C. 940 nm infrared. Up to 2 m under specified conditions.
Coverage limits
No depth map or object classification. One reading cannot clear the whole ramp area.
Calibration and firmware tests pending. Visible RYS1230 marking lasers are separate.
Notes: Q&A appendix. Outside the timed 5-minute core presentation.
Sources: hardware/esp32-s3-tof-test/README.md, Verification on 23 September 2026; artifacts/apas-tof-build/serial-powercycle-test.txt. Measurements are sensor-reported values without a known-distance accuracy comparison. Sensor specification: STMicroelectronics VL53L0X product page https://www.st.com/en/imaging-and-photonics-solutions/vl53l0x.html and DS11555 Rev 6 https://www.st.com/resource/en/datasheet/vl53l0x.pdf (pp. 1, 21–24). Single-zone ranging gives one distance per reading over I2C. The 940 nm emitter is infrared. Up to 2 m is a conditional manufacturer specification, not verified prototype range. One reading cannot prove the full ramp area clear. Visible RYS1230 marking lasers are separate from the ToF sensor. Controller adaptation and threshold/fault tests remain pending. Invalid or stale readings must block movement. Visible marking lasers do not measure range.
Presenter: ____________________
Status date: 25 September 2026. Blank result fields are intentionally incomplete.

## Slide 13
Appendix E. Machine-learning evidence
13
Module | Intended decision | Current evidence / next evidence
ML1 Assistance cue | Recognise selected observable aids. | Scripts and label guide ready. Add trained weights, held-out metrics and device latency.
ML2 Ramp zone | Camera scene cues with limited range checks. | Add camera evaluation and single-zone range tests. Full-area clearance remains unverified.
ML3 Dwell state | Classify active, clear or uncertain boarding. | Training/evaluation evidence pending. Validate the fixed-dwell sensor-clear fallback.
A detection never diagnoses disability or authorizes ramp movement by itself.
Notes: Q&A appendix. Outside the timed 5-minute core presentation.
Primary source: ../SG_GoAssist_Prototype_Action_Plan.pdf, pp. 5–8; hardware/edge-observer/README.md; hardware/edge-observer/ml1/README.md; hardware/edge-observer/ml1/LABEL_GUIDE.md. Dataset scope differs: original outline 300–500 ML1 images, later README 800–1,200. Team should confirm controlled-demo scope before capture. No measured trained-model evidence located in reviewed materials. Selected ML2 method: camera scene interpretation with VL53L0X single-zone checks in a limited monitored field. A single range cannot establish full-ramp coverage or replace object classification. Sensor specification: STMicroelectronics VL53L0X product page https://www.st.com/en/imaging-and-photonics-solutions/vl53l0x.html and DS11555 Rev 6 https://www.st.com/resource/en/datasheet/vl53l0x.pdf (pp. 1, 21–24). Single-zone ranging gives one distance per reading over I2C. The 940 nm emitter is infrared. Up to 2 m is a conditional manufacturer specification, not verified prototype range. One reading cannot prove the full ramp area clear. Visible RYS1230 marking lasers are separate from the ToF sensor.
Presenter: ____________________
Status date: 25 September 2026. Blank result fields are intentionally incomplete.

## Slide 14
Appendix F. Original deliverables D1–D5
Status against the original action plan
14
ID and owner | Deliverable | Progress / missing acceptance
D1 CE1 | Architecture, interfaces and states | Documented. Final group review pending.
D2 EE1 / EE2 / ME1 | Integrated mock bus, stop and fixture | Subsystem evidence exists. Cold-start physical trials pending.
D3 CE1 | Passenger app and dashboard | Implemented in software. Final demonstration evidence pending.
D4 CE2 / EE1 | ML1 package | Training workflow ready. Weights, metrics and model card pending.
D5 CE2 / EE1 / ME1 | ML2 and safety-fusion package | Adapt VL53L0X range and fault logic. Measured perception and safety results pending.
Notes: Q&A appendix. Outside the timed 5-minute core presentation.
Primary source: ../SG_GoAssist_Prototype_Action_Plan.pdf, p. 12. Status derives from reviewed repository evidence as of 25 September 2026. D1/D3 software availability does not establish completed hardware acceptance.
Presenter: ____________________
Status date: 25 September 2026. Blank result fields are intentionally incomplete.

## Slide 15
Appendix G. Original deliverables D6–D9
Role labels follow the outline. Assign the confirmed members to roles.
15
ID and owner | Deliverable | Progress / missing acceptance
D6 CE2 / CE1 / EE2 | ML3 or documented fallback | Trained classifier evidence pending. Validate fallback and no-premature-CLEAR cases.
D7 EE2 / ME1 | Mechanical and electrical package | CAD and circuit material available. Final BOM, power and cycle results pending.
D8 All / ME1 | Validation and accessibility report | Protocol available. Physical metrics, baseline and user findings incomplete.
D9 All / CE1 | Competition submission pack | Report and presentation drafts. Video, final evidence and packaging pending.
Notes: Q&A appendix. Outside the timed 5-minute core presentation.
Primary source: ../SG_GoAssist_Prototype_Action_Plan.pdf, p. 12; cad/VALIDATION_v2.md; hardware/INTEGRATED_PROTOTYPE.md. The draft report and this deck contribute to D9, but submission acceptance is not established.
Presenter: ____________________
Status date: 25 September 2026. Blank result fields are intentionally incomplete.

## Slide 16
Appendix H. User feedback and impact
Study findings remain incomplete
16
Study field | Evidence to add
Participants, consent and test date | 
Clarity and control | 
Confidence and comfort | 
Manual baseline versus GoAssist | 
Design changes from feedback | 
Baseline measures: acknowledgement, manual interventions, completion and waiting time.
Notes: Q&A appendix. Outside the timed 5-minute core presentation.
Primary source: ../SG_GoAssist_Prototype_Action_Plan.pdf, p. 13. Obtain consent before any participant study. If participants are classmates only, describe scenario testing rather than validation by disabled users. Compare the same scripted journey under manual assistance and GoAssist. Blank fields intentionally await actual evidence.
Presenter: ____________________
Status date: 25 September 2026. Blank result fields are intentionally incomplete.

## Slide 17
Appendix I. Costs and final evidence
Complete these fields after hardware and evidence review
17
Budget / evidence item | Confirmed value or file link
Total component cost (SGD) | 
Final BOM and power budget | 
Physical integration photos and cycle logs | 
Model metrics and model cards | 
Demo video and final source archive | 
Notes: Q&A appendix. Outside the timed 5-minute core presentation.
Primary source: ../SG_GoAssist_Prototype_Action_Plan.pdf, pp. 12, 14. Cost fields and final evidence links intentionally blank. These are editable working fields, not zero costs or completed submissions.
Presenter: ____________________
Status date: 25 September 2026. Blank result fields are intentionally incomplete.